## Slide 1: Ethyl acetate Hydrolysis
CAoo = 0,1 mol.l-1
CBoo = 0,15 mol.l-1
Batch reactor
VA = 25 l
VB = 20 l
CSTR & Plug flow
QA = 2,5 l.min-1
QB = 2 l.min-1
tBatch? VCSTR? VPF?
tBatch = 11 min 47s
Solutions
VCSTR = 350 l
VPF = 53 l
CH3COOC2H5 + OH- → CH3COO- + C2H5OH
A B
r = k CA CB with k = 7 l.mol-1.min-1
The proportions of ethyl acetate and soda introduced
in the batch reactor and in the continuous reactors
are the same
After dilution the initial concentrations are therefore
the same in the 3 reactors:
CAo = 0,056 mol.l-1
CBo = 0,066 mol.l-1

## Slide 2: Ethyl acetate Hydrolysis
CH3COOC2H5 + OH- → CH3COO- + C2H5OH
A B
Indication 1: use the concentrations after mixing
Indication 2: for each reactor make a balance on ethyl acetate (A)
Indication 3: B consumption is equal to A consumption
Indication 4: for batch and plug flow reactors, integrate after a decomposition into simple elements (it is the same)
Indices
CAoo = 0,1 mol.l-1
CBoo = 0,15 mol.l-1
After dilution
CAo = 0,056 mol.l-1
CBo = 0,066 mol.l-1
Batch reactor
VA = 25 l
VB = 20 l
CSTR & Plug flow
QA = 2,5 l.min-1
QB = 2 l.min-1
r = k CA CB avec k = 7 l.mol-1.min-1

## Slide 3: Ethyl acetate Hydrolysis
Mass balance for A in batch reactor
- k CA CB V =
Chemical production of A accumulation of A
- k CA CB =
Desired reaction rate X = 0,9
Once the two solutions are mixed, the density is constant
CA = CAo (1-X) = 0,1 CAo
A consumption = B consumption
CAo - CA = CBo - CB
- k CA ((CBo – CAo) + CA) =
t = 11 min 47s

## Slide 4: Ethyl acetate Hydrolysis
Décomposition into simple elements
-k dt =
=
Je multiplie par CA, ce qui donne:
= a
On prend CA = 0 alors: = a
Je multiplie par , ce qui donne:
=
On prend CA = - (CBo-CAo) alors: - = b
k dt =

## Slide 5: Ethyl acetate Hydrolysis
Mass balance on A in a continus stirred tank reactor
Q CAo - k CA CB V = Q CA
Inlet flow Chemical Outlet flow
rate of A production of A rate of A
Desired reaction rate X = 0,9
Once the two solutions are mixed, the density is constant
CA = CAo (1-X) = 0,1 CAo
A consumption = B consumption
CAo - CA = CBo - CB
V = 348 l
FAo, FBo
FA, FB, Fp

## Slide 6: Ethyl acetate Hydrolysis
Mass balance on A in a plug flow reactor
FA - r dV = FA + dFA
Q CA - k CA CB dV = Q CA + Q dCA
Inlet flow Chemical Outlet flow
rate of A production of A rate of A
- k CA ((CBo – CAo) + CA) dV = Q dCA
Desired reaction rate X = 0,9
Once the two solutions are mixed, the density is constant
CA = Cao (1-X) = 0,1 CAo
A consumption = B consumption
CAo - CA = CBo - CB
- k CA ((CBo – CAo) + CA) =
V = 53 l
dV
FA
FA + dFA